## Slide 1: Electric Go-Kart Data Logger
Developed by Andrew Goeden

## Slide 2: Introduction
This project was done for the Electric Vehicle Team in order to collect useful data about our go-kart for tuning and monitoring purposes.

## Slide 3: Related Work
Comparable to OBD-II used in automobiles
  https://hackaday.io/project/172214/gallery#5811103d0166235dd7eb163e87578931

## Slide 4: Challenges
I ran into a plethora of different challenges throughout the design and implementation phases
How to connect to the go-kart CAN Bus
Sending data to the client webpage without making requests (reduce latency)
What platform will be able to run the entire system locally

## Slide 5: Design

## Slide 6: Technical Details
Low-Level
Python script that reads the bytes of data from the CAN bus to send to the middleware
A MCP2515 breakout board enabled me to connect the CAN bus to the Raspberry Pi over SPI (Serial Peripheral Interface)
Middleware
NodeJS server using Express, Express-ws, and Mongoose to create a HTTP API and Websocket
Mongoose enabled me to connect to a MongoDB NoSQL database to store the data
The Express API lets me initialize a current session and sync data across the system
The Websocket lets me send data asynchronously so I can reduce latency of transmission
Web Client
ReactJS webapp using ChartJS to generate graphs to display data
WebSocket library lets me connect to the middleware and listen for messages

## Slide 7
DEMO

## Slide 8: Accomplishments & Future Work
I was able to get a complete working system that reads data from the go-kart and sends the data to the database and web app with minimal latency
Future Work:
  Migrating the middleware and web app to a server that will enable quicker startup times
  The ability to select and view different session data from the web app
  Separating the Current and Voltage graphs to better display data

## Slide 9: Thank You.
https://github.com/agoeden12/Evenger-IoT-API
https://github.com/agoeden12/Evenger-Can-Listener
https://github.com/agoeden12/evenger-react-app